## Slide 1: UNIVERSITY OF PERUGIA DEPARTMENT OF PHYSICS AND GEOLOGY PhD course in Science and Technology for Physics and Geology
PRELIMINARY PROJECT TITLE
ACQUISITION AND USE OF REMOTE INTERFEROMETRIC DATA (GBInSAR TECHNIQUE): STUDY OF THE OPEN PROBLEMS ON LANDSLIDES IN MOUNTAIN AREAS
PhD STUDENT
Saverio Romeo
TUTOR
Dott. Lucio Di Matteo
CO-TUTOR
Prof. D. Scott Kieffer
XXX cycle - Academic Year 2014/2015
Perugia, 13th February, 2015

## Slide 2: INTRODUCTION
Perugia, 13th February, 2015
Traditional monitoring instruments:
Inclinometers
Piezometers
Tiltmeters
Extensometers
Fissurometers
Topographic survey
GPS
SAR (Syntetic Aperture Radar)
GBInSAR (Ground Based InSAR)
Landslide of Termeno (Bolzano, January 2014)
Landslides represent a serious threat to human life and activities. Depending to the landslide, different monitoring instruments are available.
Forecasting the occurrence of landslide phenomena in space and time is a major scientific challenge (Manconi et al., 2014).

## Slide 3: GBInSAR EQUIPMENT
Scan length L = 2m | Maximum distance R = 4000m | Total weight ≈ 160Kg
Scan time (IBIS-FL) Δt = 5min |  | Average power consumption ≈ 60W
Perugia, 13th February, 2015
Conventionally, in GBInSAR technique, displacement is positive if the pixel moves away from the sensor and it is negative if the pixel moves towards the sensor (Hanssen, 2001).
RADAR:
RAdio Detection And Ranging
Typical spatial resolutions:
ΔR = 0,5m
ΔCR = 4,3m at 1000m
IBIS-FL Frequency:
17,1 – 17,3GHz (Ku band)

## Slide 4
Perugia, 13th February, 2015
Ground-Based Interferometric Synthetic Aperture Radar is a displacement monitoring technique developed in the late ’90 and now considered one of the most effective solutions for displacement monitoring in geology and structural fields.
(Mazzanti, 2011)
Source: Scopus
Query: Ground Based Interferometry SAR
By checking for “Ground Based Interferometry SAR” on Scopus database, several papers were published by Italian researchers in the last decade.

## Slide 5
OUTPUTS
Perugia, 13th February, 2015
Displacement map superimposed on a photo of a monitored slope and displacement time series of some pixels. (Mazzanti, 2011)

## Slide 6
Perugia, 13th February, 2015
(Romeo et al., 2014)
OUTPUTS – The Ingelsberg Landslide (Austria)
green schists

## Slide 7: PROS AND CONS
Perugia, 13th February, 2015
Main advantages
Widespread monitoring (images instead of single points);
High temporal resolution (few minutes);
Up to 0,1 mm displacement accuracy;
Effective under any weather and lighting conditions;
Fully remote monitoring (targets or sensors in the monitoring area are not required);
Long range operability (up to several km);
Fully automatic acquisition;
Suitable for real time - early warning monitoring.
Main limitations
Surface monitoring;
Limited cone of view;
Displacement monitoring along the Line of Sight;
Phase ambiguity in case of discontinuous monitoring.
Non user-friendly software for analysis (complicated interface)

## Slide 8: OPEN PROBLEMS – RELIABILITY OF GBInSAR
Perugia, 13th February, 2015
Displacement trends of extensometers and radar data for different events monitored on Ingelsberg
(Bad Hofgastein, Austria)
Despite in the last decade the use of these technologies are increased, depth analyses on the reliability of the GBInSAR measurements are lacking.
Surface displacements (GBInSAR)
Extensometer in Ingelsberg
Head Area
F5
F2
F4
F1
Map of extensometers in Ingelsberg
Displacements in depth (Extensometers)

## Slide 9: OPEN PROBLEMS – LANDSLIDE FAILURE FORECAST
Perugia, 13th February, 2015
Landslides forecasting based on displacement measurement data was introduced by Saito (1980), and developed by Voight (1989, 1990) and Fukuzono (1990).
Typical figures of the changes of the inverse number of velocity of surface displacement just before the failure
(Fukuzono, 1990)
INVERSE VELOCITY
Cinematic landslide evolution
(modified by Pellegrino et al., 1992)
Failure
No Failure
Triggering factors

## Slide 10: OPEN PROBLEMS – THE INFLUENCE OF SNOW COVER
Perugia, 13th February, 2015
During the snowfalls, areas tend to assume positive values representing an increase of distance by the radar. These anomalies may be given by the interference phenomenon of snow cover.
Path of electromagnetic waves within the snowpack
(Pieraccini et al., 2007)
European Project:
Advanced Remote Monitoring Techniques for Glaciers, Avalanches and Landslides Hazard Mitigation
In general, the dry snow is transparent to electromagnetic waves, then the waves emitted by the radar are able to penetrate through the snowpack until the underlying soil (Pieraccini et al., 2007).
GB-SAR observing the snow-covered Wattener Lizum

## Slide 11: POTENTIAL EXTERNAL PARTNERS OF THE PROJECT
Instruments
DataBase
DataBase
Experiences
Hardware and software tools useful for Time of Failure
Perugia, 13th February, 2015

## Slide 12
TRAINING IN PROGRESS
During the first year of PhD, many training activities are planned:
Lectures at the Doctoral School (Department of Physics and Geology)
Short courses:
  Introduction to R software (Department of Economics)
  Atmospheric Physics and Climate (Department of Physics and Geology)
  Magmas, Eruptions and Hazard (Department of Physics and Geology)
Course in English language (Centro Linguistico d’Ateneo)
International School:
  LARAM – Landslide Risk Assessment and Mitigation (University of Salerno)
Perugia, 13th February, 2015

## Slide 13
MANUSCRIPTS
Studio e monitoraggio dei fenomeni franosi, lectures at the course in Rilevamento geologico-tecnico e monitoraggio (9th December, 2014).
Several field trips in the context of the courses in Rilevamento geologico-tecnico e monitoraggio and Geologia ambientale (Nov - Dec, 2014)
Perugia, 13th February, 2015
INTERNATIONAL CONGRESS
Romeo S., Kieffer D.S., Di Matteo L. (2014) - The Ingelsberg landslide (Bad Hofgastein, Austria): description and first results of monitoring system (GBInSAR technique), Rendiconti Online della Società Geologica Italiana. 10/2014, 32:24-27.
OTHER ACTIVITIES
Attendance at 5th International Symposium for Geotechnical Safety and Risk (Rotterdam 13th – 15th October, 2015). 2 Papers submitted:
  Romeo S., Kieffer D.S., Di Matteo L. - Reliability of GBInSAR monitoring in Ingelsberg landslide area (Bad Hofgastein, Austria).
  Di Matteo L., Valigi D., Ricco R., Romeo S. - Effect of laboratory repeatability of direct shear test on slope stability.

## Slide 14: THANKS FOR YOUR ATTENTION!
Perugia, 13th February, 2015
“An instrument too often overlooked in our technical world is a human eye connected to the brain of an intelligent human being”.
Ralph Peck